Ausschreibungstext

Artikelnummer

208136

Typ

AXIS P7216 VIDEO ENCODER

Kurzbeschreibung

Video Netzwerk Server, 16 Eingänge, H.264, 720x576, Audio

Hauptmerkmale

16-Kanal Video-Encoder

Simultane H.264 und MJPEG Streams

Hervorragende Videoqualität

Auflösung: 720x576 Pixel (D1)

Bildrate: 25 Bilder/s.(15 fps in Quad Qview)

Hochauflösende Quad-Darstellung

Bidirektionale Audiofunktion

4x microSDHC Slot für lokale Speicher

Spannungsversorgung: 8-20VDC

Für Wand- und Rackmontage geeignet

ONVIF Konformität

Weitere Merkmale (Spezifikationen)

| Serie | Axis P72 |
| --- | --- |
| Bildauflösung max. | 720x576 |
| Bildübertragungsrate | 25 fps |
| Videoeingänge (Anzahl) | 16 |
| Kompression | H.264, M-JPEG |
| Alarmeingänge | 4 |
| Audiounterstützung | ja |
| Ethernet-Schnittstelle | 1000Base-T |
| Steuer-Schnittstellen | Ethernet, RS-422, RS-485 |
| Interner Speicher | microSD-Kartenslot |
| Bauart | 19" Einschub |
| 19" Rackmount | ja |
| Stromversorgung | 8-20VDC |
| ONVIF | ONVIF Profile S |
| Hersteller-Nummer | 0542-002 |
| Hersteller | AXIS |

Weitere Produktinformationen

Zubehör

| ACC MAINS ADAP PS-P T-C | Netzteil, 12VDC, 2A, Hohlstecker, Ersatzteil |
| --- | --- |
| ACS 1 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 1 Kanal |
| ACS 1 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 1 Kanal |
| ACS 10 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 10 Kanal |
| ACS 16 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 16 Kanal |
| ACS 20 UNIVERSAL DEVICE LIC | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 20 Kanal |
| ACS 32 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 32 Kanal |
| ACS 4 CORE DEVICE LICENSE | Axis Camera Station Software, Version 5.x Core Device, Lizenzcode, 4 Kanal |
| ACS 4 UNIVERSAL DEVICE LICENSE | Axis Camera Station Software, Version 5.x Universal Device, Lizenzcode, 4 Kanal |
| ACS CORE DEVICE E-LICENSE | Axis Camera Station Software, Core Device, E-Lizenz 1 Kanal, Sammelcode bei > 1 Stück |
| ACS UNIVERSAL DEVICE E-LICENSE | Axis Camera Station Software, Universal Device, E-Lizenz 1 Kanal, Sammelcode bei > 1 Stück |
| AXIS 4IN1 SECURITY SCREWDRIVER | Schraubendreher Set, 4-in-1, Biteinsätze pasend für Axis Produkte, inkl. Tasche |
| AXIS Companion VMS Version 4 | Video Management Software, für 16 Axis Kameras, kostenlos |
| AXIS I/O INDICATION LED 4P | Rotlicht LED, zur Montage an Axis Kameras, 4 Stück, Zubehörteil |
| AXIS LONG RANGE POE EXTENDER K | PoE Extender, PoE, PoE+, Innen, RJ45, bis 1000m Reichweite |
| AXIS SURV CARD 256GB 10 PCS | Speicherkarte, microSDXC, 256GB, Class 10, V30, inkl. SD-Adapter, 10 Stück |
| AXIS SURVEILL CARD 128GB 10PCS | Speicherkarte, microSDXC, 128GB, Class 10, 50-80 MB/s, Axis zertifiziert, 10 Stück |
| AXIS SURVEILLANCE CARD 128 GB | Speicherkarte, microSDXC, 128GB, Class 10, 50-80 MB/s, SD-Adapter, Axis zertifiziert |
| AXIS SURVEILLANCE CARD 256GB | Speicherkarte, microSDXC, 256GB, Class 10, V30, inkl. SD-Adapter |
| AXIS SURVEILLANCE CARD 64 GB | Speicherkarte, microSDXC, 64GB, Class 10, 20 MB/s, inkl. SD-Adapter, Axis zertifiziert |
| AXIS T8129 POE EXTENDER | PoE Extender, PoE, PoE+ kompatibel, RJ45, 100m Reichweite |
| AXIS T8310 CONTROL BOARD | Kontrollcenter, modular, mit Keypad, Joystick, Jog Dial |
| AXIS T8604 MEDIA CONVERTER SWI | Ethernet Medienkonverter, 2x 10/100Mbps RJ45, 2x 100/1000Mbps SFP |
| AXIS T8640 POE+ OVER COAX KIT | Medienkonverter, RJ45, BNC, Ethernet über Koax, PoE+, Base-/Device Set (2 Stück) |
| AXIS T8645 POE+ COAX COMPACT K | PoE+ über Coax Set, 1x AXIS T8641 Base Einheit, 1x AXIS T8643 Device Einheit |
| AXIS T8646 POE+ OVER COAX KIT | PoE+ OVER COAX Set, 6-Kanal: 1x T8646 POE+ OVER COAX BLADE, 6x T8642 POE+ OVER COAX DEVICE |
| AXIS T8648 POE+ COAX BLADE COM | PoE+ über Coax Set, 1x AXIS T8646 Einschubkarte, 6x AXIS T8643 Device Einheiten |

Empfehlungen

| jetcon-RJ45S-Cat6-small-FC | RJ45 Stecker Cat.6 AWG22-26, Feldkonfektionierbar, schmale und kurze Ausführung |
| --- | --- |
| WDD032G1P0C | MicroSDXC Speicherkarte, 32GB, Class 10, UHS-I U1, 16TBW, für Videoüberwachung |
| WDD064G1P0C | MicroSDXC Speicherkarte, 64GB, Class 10, UHS-I U1, 32TBW, für Videoüberwachung |
| WDD128G1P0C | MicroSDXC Speicherkarte, 128GB, Class 10, UHS-I U1, 64TBW, für Videoüberwachung |
| WDD256G1P0C | MicroSDXC Speicherkarte, 256GB, Class 10, UHS-I U1, 128TBW, für Videoüberwachung |

Dienstleistungen

| AXIS P7216 EXT.WARRANTY | Erweiterung der Gewährleistung für AXIS P7216 um 2 Jahre, max. 5 Jahre insg. |
| --- | --- |