Specifications text

Article number

238647

Type

IND-58F0028MTLA

Short description

Netzwerk Dome, Turret, Low Light, 3840x2160, Day&Night WDR, AI, 2,8mm, 12VDC, PoE, IP67

Main Features

1/1.8" Sony STARVIS CMOS sensor

Very good detail recognition even in dark areas

Maximum resolution 3840x2160 pixels, 30fps

AI analysis functions including object classification

WDR 120dB, 3D DNR noise reduction

Lens fixed focal length 2.8mm

Smart codec H.265/H.264, multi-streaming

Browser-independent (Edge, Safari, Firefox, Chrome)

Supports ONVIF profiles S/T/G

Local storage via micro SD card

Supports audio, integrated speaker and microphone

White light LED illumination, IP67

Other Features (Specifications)

| Dimensions (HxWxD) | 97,9x115,5mm |
| --- | --- |
| Series | eneo IN-Series |
| Camera Type | Face recognition, License plate recognition, People Count, Retail Intelligence |
| Resolution Standard | 8 Megapixel |
| System | 24h color |
| Sensor size | 1/1.8" |
| Imager | CMOS |
| Video compression | H.264, H.264+ (Smart Stream), H.265, H.265+ (Smart Stream), M-JPEG |
| Image resolution max. | 3640x2160 |
| Image Transmission Rate | 30 fps |
| Day&Night switch | no |
| Sensitivity | 0.0005 Lux @ F1,0 |
| Low Speed Shutter | yes |
| Digital Noise Reduction | yes |
| Backlight Compensation | BLC, HLC |
| Wide Dynamic Range (WDR) | WDR 120dB |
| Motion Detector | yes |
| Lens Type | fixed focal length |
| Focal Length | 2,8 mm |
| Iris Control | DC |
| Digital Zoom | yes |
| Horizontal Angle of View | 112° |
| Vertical Angle of View | 61° |
| MOD (Mininum Object Distance) | 0,7 m |
| llumination | White light |
| Housing | Outdoor |
| Color (housing) | Pantone P 179-1, RAL9003 |
| Hosuing material | Aluminium |
| Heater | no |
| Blower | no |
| Video outputs | no |
| Alarm inputs | no |
| Alarm outputs | no |
| Audio support | yes |
| Ethernet interface | 100Base-TX, 10Base-T |
| Serial interfaces | Ethernet |
| Internal storage | microSDHC card, microSDXC card |
| Analysis functions | Attribute Detection (AD), Cross Counting (CC), Crowd Density Detection (CD), Face Attendance (FA), Face Detection (FD), Face Recogntion (FR), Heat Map (HM), Human&Vehicle Detection (PD&VD), License Plate Detection (LPD), License Plate Recognition (LPR), Line Crossing Detection (LCD), Perimeter Intrusion Detection (PID), Queue Lenght Detection (QD), Rare Sound Detection (RSD), Stationary Object Detection (SOD) |
| Mounting | Ceiling mount, Wall mount |
| Supply voltage | 12VDC, PoE |
| Power consumption | 12VDC: max. 5,1W , PoE: max. 6,5W |
| Power over Ethernet | IEEE 802.3af |
| Vandal proof | no |
| Operating temperature | -30°C ~ +55°C, @ Humidity 95% or less (non-condensing) |
| ONVIF | ONVIF Profile G, ONVIF Profile S, ONVIF Profile T |
| Protection rating | IP67 |
| Camera type | Dome |
| Audio | 2 Way Audio, built-in loudspeaker, built-in microphone |
| Remote configuration | Browser |
| Illumination range | approx. 25m |
| Weight | 575g |
| Manufacturer order number | 238647 |
| Brand | eneo |

Additional Productinformation

Related products

| AK-21 | Camera connection box for Wall and ceiling mounting, IN Series Bullet Cameras |
| --- | --- |
| DOME-WB7 | Wall bracket for Mini Dome IND-42M2808M0A |
| eneo INsight Installation Tool | Supports adjustments for cameras with AI features for IN-series |
| eneo Site Manager | Management Software for eneo IP products |

Recommendations

| CUS-SL-F | Extra charge for special paint fixed dome in RAL color |
| --- | --- |
| eneo INsight mobile | Mobile App for recorder IN- and MN-series |
| jetcon-Cat-Cat-FC | Kabelverbinder AWG27-22, IP67 Feldkonfektionierbar |
| jetcon-RJ45S-Cat6-FC | RJ45 Stecker Cat.6 AWG22-27, Feldkonfektionierbar, schwarz |
| jetcon-RJ45S-Cat6-small-FC | RJ45 Stecker Cat.6 AWG22-26, Feldkonfektionierbar, schmale und kurze Ausführung |
| jetcon-RJ45S-Cat6A-FC | RJ45 Stecker Cat.6A AWG22-27 Feldkonfektionierbar, blau |
| jetpower-PSU-XS-11C | Universal Netzteil 12V/1,5A ID 2.1 x OD 5.5, 11mm |

Services

| CON-KAM-IPKON | Preconfiguration 1x IP camera Function test, FW update |
| --- | --- |