Specifications text

Article number

236317

Type

INT-8SF0003M0A

Short description

Network Hybrid Bullet Camera Day/Night, 2592x1944 optical, 256x192 thermal, IP66, PoE, 12V

Main Features

Dual network bullet camera

Optical resolution 2592x1944 pixels

Thermal resolution 256x192 pixels

Fixed focal 3.6mm (optical) H:81°, V:57°

Fixed focal 3.2mm (thermal) H:56°, V:42°

AI analysis functions including object classification (optical)

Temperature alarm measuring range -20°~ +150° (±8°)

Supports audio and alarm inputs and outputs

Local storage via micro SD card

Supports ONVIF profiles S, G and profile T

Power supply 12VDC or PoE IEEE 802.3af

Suitable for outdoor use IP66

Other Features (Specifications)

| Dimensions (HxWxD) | 108x91x314,6mm |
| --- | --- |
| Series | eneo IN-Series |
| Camera Type | Thermal Hybrid Bullet |
| Resolution Standard | 5 Megapixel |
| Resolution Pixels | 2560x1944, 256×192 Thermal Modul |
| System | thermal image, True Day&Night |
| Sensor size | 1/2.7" |
| Imager | CMOS |
| Video compression | H.264, H.265, M-JPEG |
| Image resolution max. | 2592x1944 |
| Thermal resolution | 256x192 |
| Image Transmission Rate | 25 fps |
| Day&Night switch | ICR |
| Sensitivity | 0,003 Lux @ F1,6 AGC on |
| Low Speed Shutter | yes |
| Digital Noise Reduction | yes |
| Backlight Compensation | BLC, HLC |
| Wide Dynamic Range (WDR) | D-WDR |
| Motion Detector | yes |
| Lens Type | fixed focal length |
| Focal Length | 3,2 mm, 3,6 mm |
| Iris Control | DC |
| Horizontal Angle of View | 56°, 81° |
| Vertical Angle of View | 42°, 57° |
| MOD (Mininum Object Distance) | 0,3 m, 2 m |
| llumination | Infrared, White light |
| Housing | Outdoor |
| Color (housing) | Pantone P 179-1, RAL9003 |
| Hosuing material | Aluminium |
| Heater | no |
| Video outputs | no |
| Alarm inputs | yes |
| Alarm outputs | yes |
| Audio support | yes |
| Ethernet interface | 100Base-TX, 10Base-T |
| Serial interfaces | Ethernet |
| Internal storage | 256GB, microSDHC card |
| Analysis functions | Cross Counting (CC), Crowd Density Detection (CD), Face Detection (FD), Fire detection, Heat Map (HM), Human (PD), Line Crossing Detection (LCD), Perimeter Intrusion Detection (PID), Queue Lenght Detection (QD), Rare Sound Detection (RSD), Stationary Object Detection (SOD), Temperature exception alarm, Vehicle (VD) |
| Mounting | Ceiling mount, Wall mount |
| Supply voltage | 12VDC, PoE |
| Power consumption | 10,2W |
| Power over Ethernet | IEEE 802.3af |
| Vandal proof | no |
| Operating temperature | -30°C ~ +60°C |
| ONVIF | ONVIF Profile G, ONVIF Profile S, ONVIF Profile T |
| Protection rating | IP66 |
| Camera type | Bullet |
| Audio | built-in loudspeaker |
| Remote configuration | Browser |
| Illumination range | approx. 15m, approx. 30m, Infrared, White Light |
| Weight | 1,45kg |
| Manufacturer order number | 236317 |
| Brand | eneo |

Additional Productinformation

Related products

| AK-20 | Camera connection box for Wall and ceiling mounting, IN Series Bullet Cameras |
| --- | --- |
| AK-21 | Camera connection box for Wall and ceiling mounting, IN Series Bullet Cameras |
| AK-24 | Dual camera connection box for Bullet or Fix Dome IN-Series cameras |
| eneo INsight Installation Tool | Supports adjustments for cameras with AI features for IN-series |
| eneo INsight mobile | Mobile App for recorder IN- and MN-series |
| eneo Site Manager | Management Software for eneo IP products |
| PM-21 | Pole mounting adapter for camera connection box AK-20 and AK-21 |
| WB-24 | Wall bracket for Dual camera connection box AK-24 |

Recommendations

| CON-KAM-IPKON | Preconfiguration 1x IP camera Function test, FW update |
| --- | --- |
| eneo INsight mobile | Mobile App for recorder IN- and MN-series |
| jetpower-PSU-XS-11C | Universal Netzteil 12V/1,5A ID 2.1 x OD 5.5, 11mm |

Services

| CON-KAM-IPKON | Preconfiguration 1x IP camera Function test, FW update |
| --- | --- |